## Slide 1: Zusammenfassung Master Thesis

## Slide 2: Challenge
Digital Twins (DTs) are key for Industry 4.0, enabling monitoring and optimization.
Simulation-Based DTs (SBDTs) are crucial for complex systems like Discrete Material Flow Systems (DMFS).
Trend towards automatically generating SBDTs from data to reduce effort.
The Challenge: How can we ensure these automatically generated SBDTs are accurate and trustworthy? Manual validation undermines the automation benefits.

## Slide 3: Problem Statement & Objective
Problem: Manual Verification, Validation, and Uncertainty Quantification (VVUQ) of automatically generated SBDTs is inefficient, costly, and hinders scalability. Lack of standardized methods creates a trust deficit.
Objective: Develop and evaluate a data-driven framework for automated VVUQ of automatically generated SBDTs, focusing on DMFS.
Research Questions: RQ1: Efficient implementation of automated VVUQ?
RQ2: Best data-driven approaches for discrepancy detection?
RQ3: Improvement over traditional methods?

## Slide 4: Traditional VVUQ is bad!
Manual Effort: Highly labor-intensive, requires domain experts.
Scalability Issues: Difficult to apply continuously or frequently, especially with evolving SBDTs.
Subjectivity: Expert reviews can be subjective.
Inefficiency: Undermines the cost/time benefits promised by automated SBDT generation.

## Slide 5: ML-based!
Idea: Treat validation as a supervised classification problem (not as unsupervised see Dos Santos 2024)
Input Data: Process execution data from Real System and Simulated SBDT, formatted as Object-Centric Event Logs (OCEL).
Labels: Assign different labels (e.g., Real = 1, Simulated = 0).
Classifier: Train an ML model (e.g., BiLSTM) to distinguish between the two data sources based on feature subsets representing SBDT components (time, resources, process flow etc.).

## Slide 6: The Reversed Interpretation: Performance NOT-EQ Fidelity
Traditional ML Goal: High accuracy/AUC = Good model performance.
Our Validation Goal: Assess SBDT fidelity.
The Key Insight:
  IF Classifier performs POORLY (AUC ≈ 0.5): It cannot distinguish real vs. simulated data. => HIGH SBDT Fidelity (The twin successfully mimics reality for those features).
  IF Classifier performs WELL (AUC >> 0.5): It can easily distinguish real vs. simulated data. => LOW SBDT Fidelity (The twin failed to replicate real-world complexity/patterns).
High classifier performance signals detectable discrepancies in the SBDT component being tested.

## Slide 7: Multi Ensemble Approach!
Models Used:
  Whitebox Baseline: Decision Tree (DTree) - Interpretable.
  Blackbox: ResNet-BiLSTM-Attention - Captures sequential patterns.
Statistical Significance: How confident are we that the classifier isn't just guessing?
Permutation Testing:
  Shuffle labels randomly many times (simulating "no difference") => H0
  Calculate classifier performance (AUC) on shuffled data to get a "null distribution".
  Compare observed AUC to null distribution => p-value.
  Low p-value (< α): Observed AUC is unlikely random => Statistically Significant Difference Found.
  Repeat multiple runs => Rejection Rate (RR): How consistently is the difference found?
Applied on IoT Factory Data!

## Slide 8: Put Features into Feature Subsets = Model Components in Framework Schwede & Fischer 2024
Time Model:
  Features: duration, start_time, end_time, and other engineered time features (e.g., cyclical encodings).
Transition Model:
  Features: process_id, resource_id, end_time.
Transformation Model:
  Features: part_id.
Quality Model:
  Note: Quality information excluded in the current validation model.
Resource Model:
  Features: resource_id, process_id, part_id.
Resource Capacity Model:
  Features: resource_id.
  Note: Insufficient data available for detailed capacity modelling in this study.
Process Model:
  Features: process_id, part_id, resource_id.

## Slide 9: Key Result: Detecting Discrepancies
Permutation Test Results (BiLSTM, α=0.01)
High Mean ROC AUC scores observed for most SBDT components (e.g., Time: 0.9998, Transition: 1.0000, Process: 0.9788).
Very Low Mean p-values (often ≈ 0.0000).
High Rejection Rates (RR ≥ 0.80 for all components, often 1.00).
Similar significant results found with the Whitebox (DTree) model.

## Slide 10: Interpretation: Framework Successfully Identifies Inaccuracies
Both ML models consistently and statistically significantly distinguished between real and simulated data across all tested SBDT components.
Conclusion (Based on Reversed Interpretation): The current configuration of the OFacT SBDT exhibited detectable inaccuracies compared to the real IoT Factory data for aspects like time model, resource usage, process flow etc.
Value: The framework worked as intended – it successfully shows where the SBDT's fidelity was lacking, providing targeted feedback for improvement.

## Slide 11: Weitere Ansätze siehe Email
Contribution und Impact: A scalable, objective, statistically-grounded method for validating SBDTs component-wise.
Limits: Single Case Study, Focus on Validation, High efforts for data pipeline, Twin createion, UQ only with p-values => Choose MCD or BNN

## Slide 12: Features Gesamtübersicht

## Slide 13: OCEL Format

## Slide 14: Automated Framework